Directions to install and use of UW-PCS OPNET simulation modules

Aug 26th, 2006

Hui Ma

mahui@ee.washington.edu

University of Washington

1: Unzip the archive file

2: Make a backup of current “wlan_support.h” in

“C:\Program Files\OPNET\11.0\models\std\include”

3: Copy “wlan_support.h” in the archive to

“C:\Program Files\OPNET\11.0\models\std\include”

4: Copy

- Wlan_station_PCS_ED_060217.nd.m ( the MAC layer node model)

- Wlan_mac_pcs_ED_060217.pr.m (the MAC processing model)

To       “C:\Documents and Settings\**********(UserName)\op_models”

5: Copy

- Wlan_power_inside_building_pcs_ED_051202.ps.c ( Power pipeline stage model)

- Wlan_ecc_pcs_ED_051202.ps.c (ECC pipeline stage model)

- Wlan_ber_EBN0.ps.c (BER pipeline stage model)

To       “C:\Program Files\OPNET\11.0\models\std\wireless_lan”

6: Now you can use the node model “Wlan_station_PCS_ED_060217”.

- PCS threshold and Receiver Sensitivity will be inputted by “Carrier Sensing threshold (dBm)” and “Packet Reception-Power Threshold” (the original threshold provide by default OPNET) respectively. Both them use the unit of dBm.

- Path Loss Exponent is also a configurable parameter, which will be automatically read into pipeline stages.

7: If you want to use this model in new node models, please refer to the MAC, RX and TX processing models in Wlan_station_PCS_ED_060217.nd.m.

8: If you want to know more details about this module, please check the file of “OPNETWORK06_v4.pdf”, which is a paper titled “Analysis and Simulation Model of Physical Carrier Sensing in IEEE 802.11Mesh Networks” and presented on OPNETWORK 2006, Washington, DC, Aug 28-Sep 1, 2006. The code provided here is consistent with the model described in this paper.

9: Enjoy!

Statement: In case that you use and/or modify any code provided at this package for your own research and subsequent publications, we request that you a) provide a suitable acknowledgement and b) provide us with a copy of your code.