## Slide 1: Introduction to Optimization (Part 2)
Daniel Kirschen

## Slide 2: Optimization with inequality constraints
Objective function
Equality constraints
Inequality constraints

## Slide 3: Example: Economic Dispatch
L
G1
G2
x1
x2
Inequality constraints
Equality constraints

## Slide 4: Example: Economic Dispatch
x1max
x1min
x2min
x2max
x1
x2
Family of ellipses
A
Ellipse tangent to equality constraint at A
Inequality constraints are satisfied

## Slide 5: Example: Economic Dispatch
x1
x2
x1max
x1min
x2min
x2max
A
Ellipse tangent to equality constraint at B
Inequality constraints are NOT satisfied!
What is the solution for a larger load?
B

## Slide 6: Example: Economic Dispatch
x1
x2
x1max
x1min
x2min
x2max
A
C is the solution because it is the point on the equality constraint that satisfies the inequality constraints at minimum cost
B
C

## Slide 7: Binding Inequality Constraints
A binding inequality constraint is an inequality constraint that is satisfied exactly
Example:
  If we must have x1 ≤ x1max
  And at the solution we have x1 = x1max
  Then the constraint x1 ≤ x1max is said to be binding
ALL of the inequality constraints must be satisfied
Only a FEW will be binding (or active) at any given time
But we don’t know ahead of time which inequality constraints will be binding!
All equality constraints are always binding

## Slide 8: Solution using Lagrange multipliers
Lagrangian function:

## Slide 9: Optimality Conditions
Complementary Slackness Conditions
(Known as the Karush Kuhn Tucker or KKT conditions)

## Slide 10: Complementary slackness conditions
Two possibilities for each constraint j:
OR

## Slide 11: Solving the problem
The KKT conditions are not quite enough to solve the problem
The complementary slackness conditions:
  Tell us that an inequality constraint is either binding or non-binding
  DON’T tell us which constraints are binding and non-binding
The binding constraints have to be identified through trial and error

## Slide 12: Example

## Slide 13: Example
x1
x2

## Slide 14: Example

## Slide 15: Example
KKT conditions do not tell us if inequality constraint is binding
Must use a trial and error approach
Trial 1: Assume inequality constraint is not binding μ = 0
From solution of example without inequality constraint, we know that the solution is then:
This solution is thus not an acceptable solution
Inserting these values in the inequality constraint, we get:

## Slide 16: Example
Trial 2: Assume that the inequality constraint is binding
All KKT conditions are satisfied. This solution is acceptable

## Slide 17: Example: graphical solution
x1
x2
Solution of problem with inequality constraint
Solution of problem without inequality constraint
Solution of problem without constraints

## Slide 18: Application to Economic Dispatch
L
G1
G2
x1
x2

## Slide 19: Application to Economic Dispatch
KKT Conditions:

## Slide 20: Application to Economic Dispatch
KKT Conditions (continued):

## Slide 21: “Solving” these equations
Trial #1: No generator is at a limit
No inequality constraint is binding and all μ’s are equal to zero
All generators operate at the same incremental cost

## Slide 22: Solving the KKT Equations
Trial #2: Generator 1 is at its upper limit; Other limits not binding
All generators do NOT operate at the same incremental cost!
The incremental cost of unit 1 is lower…. Why?
If that was possible, more power would be produced by unit 1

## Slide 23: Solving the KKT Equations
Trial #3: Generator 1 is at its lower limit; other limits not binding
Again, all generators do NOT operate at the same incremental cost!
The incremental cost of unit 1 is higher… Why?
If that was possible, less power would be produced by unit 1

## Slide 24: Physical interpretation of the Lagrangian
Where is either an equality constraint or a binding inequality constraint
The optimum values of the decision variables and the Lagrange multipliers are given by the optimality conditions:
Lagrangian:

## Slide 25: What happens when I move the constraint?
Equality constraint:
Inequality constraint:
Keep sufficiently small that an optimal solution still exists and involves the same binding inequality constraints
The optimal value of the decision variables and of the Lagrange multipliers change as changes:

## Slide 26: What happens when I move the constraint?
Lagrangian:
Re-arranging the terms, we get
= 0
At the optimum:
= 0

## Slide 27: Physical interpretation of the Lagrangian
= 0
Complementary slackness 
At the optimum:
The value of the Lagrangian function is thus equal to the value of the cost or objective function at the optimum
The value of the Lagrange multipliers at the optimal solution thus tell us by how much the the objective changes when the constraints change
The Lagrange multipliers are the marginal cost of the constraints

## Slide 28: Physical Interpretation of Lagrange Multipliers
The Lagrange multipliers are thus often called shadow costs
Non-binding inequality constraints have a zero marginal cost
Adding binding constraints always increases the cost of a solution
Tightening a constraint increases the cost
Relaxing a constraint decreases the cost

## Slide 29: Physical Interpretation of Lagrange Multipliers
Note that these observations are valid only for sufficiently small changes in the constraints
If the constraints change substantially, the set of constraints that is binding at the optimum may change
The constraints that are no longer binding would then have a zero marginal cost
The newly binding constraints would then have a non-zero marginal cost

## Slide 30
Example: Economic Dispatch Using Lagrange Multipliers

## Slide 31: Example: Economic Dispatch
A load L = 800 MW is supplied by three generating units.
The cost characteristics of these generating units are
given by the following expressions:
C1 = 100 + 8 P1 + 0.1 P12 [$/h] 230 ≤ P1 ≤ 400 MW
C2 = 200 + 7 P2 + 0.06 P22 [$/h] 100 ≤ P2 ≤ 500 MW
C3 = 250 + 9 P3 + 0.07 P32 [$/h] 100 ≤ P3 ≤ 260 MW
Calculate the optimal economic dispatch.

## Slide 32: Example: Form the Lagrangian

## Slide 33: Example: Optimality Conditions
Set the partial derivatives of the Lagrangian with respect to the decision variables and λ to zero:
(1)
(2)
(3)
(4)

## Slide 34: Example: Optimality Conditions
Set the partial derivatives of the Lagrangian with respect to the μ’s to zero:

## Slide 35: Example: Optimality Conditions
Set the partial derivatives of the Lagrangian with respect to the μ’s to zero:

## Slide 36: Example: Complementary slackness

## Slide 37: Example: First Trial (1)
Assume that none of the inequality constraints is binding
This means that all the μ‘s are zero
Set the μ’s equal to zero in the optimality conditions.
Equations (1) to (3) become:

## Slide 38: Example: First Trial (2)
Inserting these expressions in Equation (4), we get:
With L = 800MW, we get:
Replacing λ in the equations on the previous slide, we have:
Not a valid solution
 trial fails

## Slide 39: Example: Second Trial (1)
We must try another combination of binding constraints.
Let us try:
6 inequality constraints  26 = 64 possible combinations
Realistic system  ridiculously large number of combinations
Must use information from previous trials

## Slide 40: Example: Second Trial (2)
However, we must check that the μ‘s meet the complementary slackness conditions

## Slide 41: Example: Second Trial (3)

## Slide 42: Example: Second Trial (4)
The constraint
should not be binding!
What is happening?
First trial:

## Slide 43: Example: Second Trial (5)
Second trial:
In the second trial, we “pushed” P1 towards its lower limit and P3 towards its upper limit. However, there was no need to push P3 because increasing P1 would naturally reduce P3 below its limit.

## Slide 44: Example: Third Trial (1)

## Slide 45: Example: Third Trial (2)
Solution that satisfies all the optimality conditions:
 Cost of an extra MW of load
 Value of reducing by 1MW

## Slide 46: Example: Optimal Solution
Third trial:

## Slide 47: Practical Economic Dispatch

## Slide 48: Equal Incremental Cost Dispatch
PA
PB
PC
+

## Slide 49: Lambda search algorithm

## Slide 50: Linear Cost Curves
PA
PB
PAMAX
PBMAX
PA
PB
PAMAX
PBMAX

## Slide 51: Linear Cost Curves
PA
PB
PA
PB
PAMAX
PBMAX
PAMAX
PBMAX

## Slide 52: Linear Cost Curves
PA
PB
PA
PB
PAMAX
PBMAX
PAMAX
PBMAX

## Slide 53: Linear Cost Curves
The output of the unit with the lowest incremental cost (in this case unit A) is increased first (it is “loaded” first)
The output of the other units is not increased until unit A is loaded up to its maximum
The output of the unit with second lowest incremental cost is then increased (i.e. the “second cheapest” unit)
And so on until the generation meets the load

## Slide 54: Linear cost curves with minimum generation
PA
PB
PA
PB
PAMAX
PBMAX
PBMIN
PAMIN
PAMAX
PBMAX
PBMIN
PAMIN

## Slide 55: Linear cost curves with minimum generation
All generating units are first loaded up to their minimum generation
The generating units are then loaded in order of incremental cost

## Slide 56: Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 57: Economic Dispatch with Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 58: Economic Dispatch with Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 59: Economic Dispatch with Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 60: Economic Dispatch with Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 61: Economic Dispatch with Piecewise Linear Cost Curves
PA
PB
PA
PB

## Slide 62: Economic Dispatch with Piecewise Linear Cost Curves
All generators except one are at breakpoints of their cost curve
The marginal generator is between breakpoints to balance the load and generation
Not well-suited for lambda-search algorithm
Very fast table lookup algorithm:
  Rank all the segments of the piecewise linear cost curves in order of incremental cost
  First dispatch all the units at their minimum generation
  Then go down the table until the generation matches the load

## Slide 63: Example
PA
PB
20
30
70
80
110
120
140
150
0.1
0.6
0.8
0.3
0.5
0.7
If Pload = 210MW
The optimal economic dispatch is:
PA = 120MW
PB = 90 MW
λ = 0.6